## Slide 1
Latches, Flip-Flops,
and Timers
7

## Slide 2: 触发器(flip flop) vs 锁存器（latch）
behavior is the same unless input
changes while the clock is high
CLK
D
Qff
Qlatch
D Q
Q
CLK
D Q
Q
CLK

## Slide 3
A latch is a temporary storage device that has two stable states (bistable). It is a basic form of memory.
Latches
The S-R (Set-Reset) latch is the most basic type. It can be constructed from NOR gates or NAND gates. With NOR gates, the latch responds to active-HIGH inputs; with NAND gates, it responds to active-LOW inputs.
NOR Active-HIGH Latch NAND Active-LOW Latch
R
S
Q
Q
Q
S
R
Q

## Slide 4
The active-HIGH S-R latch is in a stable (latched) condition when both inputs are LOW.
Latches
R
S
Q
Q
Assume the latch is initially RESET (Q = 0) and the inputs are at their inactive level (0). To SET the latch (Q = 1), a momentary HIGH signal is applied to the S input while the R remains LOW.
0
1
0
R
S
Q
Q
1
0
0
To RESET the latch (Q = 0), a momentary HIGH signal is applied to the R input while the S remains LOW.
0
0
1
0
1
0
Latch initially RESET
Latch initially SET

## Slide 5
S
R
The active-LOW S-R latch is in a stable (latched) condition when both inputs are HIGH.
Latches
Q
Q
1
1
0
1
0
1
Latch initially RESET
Q
Q
1
1
0
1
0
1
Latch initially SET
S
R
Assume the latch is initially RESET (Q = 0) and the inputs are at their inactive level (1). To SET the latch (Q = 1), a momentary LOW signal is applied to the S input while the R remains HIGH.
To RESET the latch a momentary LOW is applied to the R input while S is HIGH.
Never apply an active set and reset at the same time (invalid).

## Slide 6
The FUNCTION TABLE
S | R | Qn | Qn+1 | function
0 | 0 | 0 | ╳ | forbid
0 | 0 | 1 | ╳ | 
0 | 1 | 0 | 1 | set “1”
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | set “0”
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 0 | keep
1 | 1 | 1 | 1 | 

## Slide 7: Karnaugh map
The behavioral equation of basic RS flip-flop
Qn+1=S+RQn
R+S=1 (restraint equation)

## Slide 8
Simplification function table
R | S | Qn+1 | FUNCTION
0 | 0 | ╳ | FORBID
0 | 1 | 0 | SET “0”
1 | 0 | 1 | SET “1”
1 | 1 | Qn | KEEP

## Slide 9
Movement characteristics
The basic RS flip-flop’s output port Q and Q
are determined by R and S.When the input signal
R and S are changed,output port Q and Q are
changed correspondingly.
Waveform
R
S
Q
Q

## Slide 10
A gated latch is a variation on the basic latch.
Latches
The gated latch has an additional input, called enable (EN) that must be HIGH in order for the latch to respond to the S and R inputs.
R
S
Q
Q
EN
Show the Q output with relation to the input signals. Assume Q starts LOW.
Example
Solution
Keep in mind that S and R are only active when EN is HIGH.
S
R
EN
Q

## Slide 11: Logical function
cp
1
1
1
1
1
1
1
1
0
function
keeping
keeping
Set’0’
Set’1’
forbid

## Slide 12: Karnaugh map
S
RQn
0
1
0
0
╳
1
1
╳
0
1
00
01
11
10
Qn+1=S+RQn
R·S=0 (restraint equation)
Behavioral equation
(When CP=1)

## Slide 13
Logical symbol
R
S
Q
CP
Q

## Slide 14
Waveform
Q
Q
S
R
CP

## Slide 15
Waveform
S
R
CP
Q
Q

## Slide 16
Latches
The D latch is an variation of the S-R latch but combines the S and R inputs into a single D input as shown:
A simple rule for the D latch is:
Q follows D when the Enable is active.
D
EN
Q
Q
Q
Q
D
EN

## Slide 17
Work principle
From the circuit,we can get:
S=D R=D
Substitute the behavioral equation of R-S
synchronous flip-flop ,we get:
Qn+1=S+RQn
=D+DQn
=D (When CP=1)

## Slide 18
Latches
The truth table for the D latch summarizes its operation. If EN is LOW, then there is no change in the output and it is latched.

## Slide 19
Latches
Determine the Q output for the D latch, given the inputs shown.
Notice that the Enable is not active during these times, so the output is latched.
Q
Q
D
EN
Example

## Slide 20
Flip-flops
A flip-flop differs from a latch in the manner it changes states. A flip-flop is a clocked device, in which only the clock edge determines when a new bit is entered.
The active edge can be positive or negative.
Dynamic input indicator

## Slide 21
Flip-flops
The truth table for a positive-edge triggered D flip-flop shows an up arrow to remind you that it is sensitive to its D input only on the rising edge of the clock; otherwise it is latched. The truth table for a negative-edge triggered D flip-flop is identical except for the direction of the arrow.
(a) Positive-edge triggered (b) Negative-edge triggered

## Slide 22
(1)接收信号：
CP = 1
主触发器接收输入信号
主触发器跟随D变化
(2) 输出信号：
CP = 0
主触发器保持不变；
从触发器由CP到来之前的
QnM 确定。
即：
下降沿时刻有效
G7
CP
Q
&
&
Q
G3
&
&
D
G2
G4
&
&
&
&
G6
G8
1
G1
G5
1
1
QM
QM
Negative edge-triggered DFF

## Slide 23
Flip-flops
The J-K flip-flop is more versatile than the D flip flop. In addition to the clock input, it has two inputs, labeled J and K. When both J and K = 1, the output changes states (toggles) on the active clock edge (in this case, the rising edge).

## Slide 24
Flip-flops
Determine the Q output for the J-K flip-flop, given the inputs shown.
Example
CLK
Q
K
J
CLK
K
J
Q
Q
Notice that the outputs change on the leading edge of the clock.
Solution
Set
Toggle
Set
Latch

## Slide 25
Flip-flops
CLK
D
CLK
Q
Q
A D-flip-flop does not have a toggle mode like the J-K flip-flop, but you can hardwire a toggle mode by connecting Q back to D as shown. This is useful in some counters as you will see in Chapter 8.
For example, if Q is LOW, Q is HIGH and the flip-flop will toggle on the next clock edge. Because the flip-flop only changes on the active edge, the output will only change once for each clock pulse.
D flip-flop hardwired for a toggle mode

## Slide 26
边沿 JK 触发器
一、电路组成及符号
二、工作原理
QM
QM
CP
R
S
Q
Q
S C1 R
R
S
C1
1
1
1
D
>1
>1
&
J
K
冗余项
国
标
符
号
Q
Q
CP
C1
1J IK
J K
Q
Q
CP
CP
J K
J K
曾
用
符
号
CP 下降沿有效
Q =JQ + KQ

## Slide 27
Flip-flops
Synchronous inputs are transferred in the triggering edge of the clock (for example the D or J-K inputs). Most flip-flops have other inputs that are asynchronous, meaning they affect the output independent of the clock.
Two such inputs are normally labeled preset (PRE) and clear (CLR). These inputs are usually active LOW. A J-K flip flop with active LOW preset and CLR is shown.
CLK
K
J
Q
Q
PRE
CLR

## Slide 28
Flip-flops
Flip-flops
Determine the Q output for the J-K flip-flop, given the inputs shown.
Example
CLK
K
J
Q
Q
PRE
CLR
Solution
Set
Toggle
Reset
Toggle
Set
Set
Reset
Latch
CLK
K
J
Q
PRE
CLR

## Slide 29
R
S
Q
Q
R
S
Q
Q
EN
Q
Q
D
EN
CLK
K
J
Q
Q
CLK
K
J
Q
Q
PRE
CLR

## Slide 30
The logic function expression method of flip-flop
There are state table、karnaugh map、behavioral equation、
state diagram and sequential diagram to express the function
of flip-flop. We will use edge-triggered D flip-flop and edge-
triggered J-K flip-flop to explain them.
D
C
Q
Q
C
J
K
Q
Q
edge-triggered D flip-flop
edge-triggered J-K flip-flop

## Slide 31
1 state table
State table also names truth table. It describes the
flip-flop’s logic function by the form of table.
⑴ D flip-flip’s state table
D
0
1
Q
0
1
NOTE
Set 0
Set 1
It express directly D flip-flop that has the function
of set 0 and set 1.

## Slide 32
⑵ J-K flip-flip’s state table
J K
0 0
0 1
1 0
1 1
Q
Qn
0
1
Qn
NOTE
KEEPING
Set 0
Set 1
TOGGLE
It express directly J-K flip-flop that has the function
of keeping, set 0 , set 1 and toggle.

## Slide 33
2 Karnaugh map
⑴ D flip-flip’s Karnaugh map
D flip-flip’s next state is only determined by D. It is a
function with single variable, so it’s karnaugh map has
no value.
⑵ J-K flip-flip’s Karnaugh map
JK
Q
n
0
1
00
01
11
10
0
0
0
0
1
1
1
1

## Slide 34
3 Behavioral equation
⑴ D flip-flip’s behavioral equation
Q =D
n+1
It can get from state stable directly.
⑵ J-K flip-flip’s behavioral equation
Q =JQ + KQ
n+1
n
n

## Slide 35
4 State diagram
State diagram has characteristic of view-direct. It makes
flip-flop’s state transition and transition condition expressed
with geometric figure.
⑴ D flip-flip’s state diagram
0
1
D
= 0
D
= 0
D
= 1
D
= 1

## Slide 36
⑵ J-K flip-flip’s state diagram
K=1

## Slide 37
5 sequential diagram
⑴ D flip-flip’s sequential diagram
CLK
D
Q

## Slide 38
⑵ J-K flip-flip’s sequential diagram
CLK
J
K
Q

## Slide 39
Conversion of flip-flops
Flip-flops can classify RS flip-flop, JK flip-flop, D flip-flop,
T flip-flop and T’ flip-flop according to their function.
1 T and T’ flip-flop
⑴ T’ flip-flop: It can only realize toggle function, also named
toggle flip-flop and counter flip-flop, namely when a clock
pulse comes, it’s state changes once.
⑵ T flip-flop: It has the function of keeping and toggle ,and
it has a control end T.
When T=0, keeping.
When T=1, toggle.

## Slide 40
T flip-flop function description
Truth table
T Qn+1
0 Qn
1 Qn
Behavioral table
Qn T Qn+1
0 0 0
0 1 1
0 1
1 1 0
Behavioral function

## Slide 41
2 Conversion of flip-flop
Conversion method: ask logic conversion circuit
Namely original input end
through conversion
circuit
new flip-flop input end
⑴ JK flip-flop’s conversion( D, T, T’)
JK flip-flop
D flip-flop
So J=D,K=D, convert D flip-flop.
Q
J
cp
K
1J
C1
1K
Q
&
D

## Slide 42
T flip-flop
So J=T, K=T, convert T flip-flop.
T’ flip-flop
When J=K=1, convert T’ flip-flop.
Q
J
cp
K
1J
C1
1K
Q
T

## Slide 43
⑵D flip-flop’s conversion( JK, T, T’)
D flip-flop：
JK flip-flop
So D=
n
n
n
Q
K
Q
J
Q
+
=
+
1
n
n
Q
K
Q
J
+
,convert JK flip-flop.
&
J
≥1
&
&
Q
D
cp
1D
C1
Q
K

## Slide 44
T flip-flop
So
Q
T
D
Å
=
n
,convert T flip-flop.
T’ flip-flop
T
=1
Q
D
cp
1D
C1
Q
Q
D
cp
1D
C1
Q

## Slide 45
Request
1 Master skilled kinds of flip-flop’s function characteristics,
truth table, behavioral equation, state diagram and
sequential diagram.
2 Master conversion of flip-flops.

## Slide 46
Example
For the following truth table, please realize it with JK
flip-flop and other gates.
A B | Qn＋1
0 0 0 1 1 0 1 1 | Qn 1 Qn 0
Solution:
n
n
n
Q
K
Q
J
Q
+
=
+
1
B
A
K
A
J
Å
=
=
\

## Slide 47
Other specifications include maximum clock frequency, minimum pulse widths for various inputs, and power dissipation. The power dissipation is the product of the supply voltage and the average current required.
Flip-flop Characteristics
A useful comparison between logic families is the speed-power product which uses two of the specifications discussed: the average propagation delay and the average power dissipation. The unit is energy.
Example
Solution
What is the speed-power product for 74AHC74A? Use the data from Table 7-5 to determine the answer.
From Table 7-5, the average propagation delay is 4.6 ns. The quiescent power dissipated is 1.1 mW. Therefore, the speed-power product is
5 pJ

## Slide 48
Flip-flop Applications
Principal flip-flop applications are for temporary data storage, as frequency dividers, and in counters (which are covered in detail in Chapter 8).
Typically, for data storage applications, a group of flip-flops are connected to parallel data lines and clocked together. Data is stored until the next clock pulse.
Parallel data input lines
Clock
Clear
Output lines
Q0
Q1
Q2
Q3

## Slide 49
Flip-flop Applications
For frequency division/counter, it is simple to use a flip-flop in the toggle mode or to chain a series of toggle flip flops to continue to divide by two.
One flip-flop will divide fin by 2, two flip-flops will divide fin by 4 (and so on). A side benefit of frequency division is that the output has an exact 50% duty cycle.
HIGH
HIGH
CLK
K
J
QA
CLK
K
J
fin
QB
fout
Waveforms:
fin
fout

## Slide 50
One-Shots
The one-shot or monostable multivibrator is a device with only one stable state. When triggered, it goes to its unstable state for a predetermined length of time, then returns to its stable state.
For most one-shots, the length of time in the unstable state (tW) is determined by an external RC circuit.
Trigger
CEXT
REXT
+V
CX
RX/CX
Q
Q
tW
Trigger
Q

## Slide 51
One-Shots
Retriggerable one-shots respond to any trigger, even if it occurs in the unstable state. If it occurs during the unstable state, the state is extended by an amount equal to the pulse width.
Retriggers
tW
Trigger
Q
Retriggerable one-shot:
Nonretriggerable one-shots do not respond to any triggers that occur during the unstable state.

## Slide 52
One-Shots
An application for a retriggerable one-shot is a power failure detection circuit. Triggers are derived from the ac power source, and continue to retrigger the one shot. In the event of a power failure, the one-shot is not triggered and an alarm can be initiated.
tW
tW
tW
Retriggers
Retriggers
Triggers derived from ac
Q
Missing trigger due to power failure
Power failure indication

## Slide 53
The 555 timer
The 555 timer can be configured in various ways, including as a one-shot. A basic one shot is shown. The pulse width is determined by R1C1 and is approximately tW = 1.1R1C1.
The trigger is a negative-going pulse.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
tW = 1.1R1C1
C1
R1

## Slide 54
The 555 timer
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
+VCC
tW = 1.1R1C1
C1
R1
Determine the pulse width for the circuit shown.
Example
Solution
tW = 1.1R1C1 = 1.1(10 kW)(2.2 mF) =
10 kW
2.2 mF
24.2 ms
+15 V

## Slide 55
The 555 timer
The 555 can be configured as a basic astable multivibrator with the circuit shown. In this circuit C1 charges through R1 and R2 and discharges through only R2. The output frequency is given by:
The frequency and duty cycle are set by these components.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
C1
R1
R2
+VCC

## Slide 56
The 555 timer
Given the components, you can read the frequency from the chart. Alternatively, you can use the chart to pick components for a desired frequency.
RESET
DISCH
THRES
TRIG
GND
CONT
OUT
VCC
C1
R1
R2
+VCC
C1 (mF)
f (Hz)

## Slide 57
Latch
Bistable
Clock
D flip-flop
J-K flip-flop
A bistable digital circuit used for storing a bit.
Having two stable states. Latches and flip-flops are bistable multivibrators.
A triggering input of a flip-flop.
A type of bistable multivibrator in which the output assumes the state of the D input on the triggering edge of a clock pulse.
A type of flip-flop that can operate in the SET, RESET, no-change, and toggle modes.
Selected Key Terms