## Slide 1
Computer Networks
Fall 2021
Chapter 6
The Link Layer and LANs

## Slide 2: 因特网协议层次结构
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
光纤，铜质电缆，无线链路
数据信号

## Slide 3: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 4: Link layer: introduction
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired
  wireless
  LANs
layer-2 packet: frame, encapsulates datagram
mobile network
enterprise
network
national or global ISP
datacenter
network
link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, fiber the next link, Ethernet at destination
each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm

## Slide 6: Link layer: services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)
reliable delivery between adjacent nodes
  we already know how to do this!
  seldom used on low bit-error links (如光纤和双绞线电缆)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?
…
…
A：出错率高，如果在链路层不做差错控制工作，漏出去的错误比较高；到了上层如果需要可靠控制的数据传输代价会很大

## Slide 7: Link layer: services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
error correction:
  receiver identifies and corrects bit error(s) without retransmission
half-duplex and full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time
…
…

## Slide 8: Where is the link layer implemented?
in each-and-every host
  也在每个路由器上
  交换机的每个端口上
link layer implemented in network interface card (NIC) or on a chip
  Ethernet, WiFi card or chip
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical

## Slide 9: Interfaces communicating
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram

## Slide 10: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 11: Error detection
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 12: Parity checking
single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
two-dimensional bit parity:
detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
1 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: set parity bit so there is an even number of 1’s
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 13: Internet checksum (review)
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 14: Cyclic Redundancy Check (CRC)
more powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given)
goal: choose r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
r CRC bits
d data bits
D
R
<D,R> = D 2r XOR R
*
bit pattern
formula for bit pattern

## Slide 15: Cyclic Redundancy Check (CRC): example
We want:
  D.2r XOR R = nG
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
D.2r
G
R = remainder [ ]
or equivalently:
  D.2r = nG XOR R
or equivalently:
if we divide D.2r by G, want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1

## Slide 16: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 17: Multiple access links, protocols
two types of “links”:
point-to-point
  point-to-point link between Ethernet switch, host
  PPP （point-to-point protocol） for dial-up access
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/5G. satellite
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G

## Slide 18: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
  用于传输控制信息
multiple access protocol

## Slide 19: An ideal multiple access protocol
given: multiple access channel (MAC) of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 20: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 21: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in “rounds”
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
Equal rate = R/N, long latency even if only one node transmitting
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 22: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 23: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes: “collision”
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 24: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with probability p until success
randomization – why?

## Slide 25: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots (即使有帧要发送，仍然有可能存在空闲的时隙)
nodes may be able to detect collision in less than time to transmit packet
即使已经检测到冲突，当前的帧必须传完
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
C: collision
S: success
E: empty

## Slide 26: Slotted ALOHA: efficiency
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
suppose: N nodes with many frames to send, each transmits in slot with probability p
  prob that given node has success in a slot = p(1-p)N-1
  prob that any node has a success = Np(1-p)N-1
  max efficiency: find p* that maximizes Np(1-p)N-1
  for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
at best: channel used for useful transmissions 37% of time!

## Slide 27: Pure ALOHA
unslotted Aloha: simpler, no synchronization
  when frame first arrives: transmit immediately
collision probability increases with no synchronization:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]
t0 + 1
t0 - 1
t0
will overlap
with end of
i’s frame
will overlap
with start of
i’s frame
pure Aloha efficiency: 18% !

## Slide 28: Pure ALOHA
假设发射一帧的时间为T0，在一帧的传输时间内平均有G个帧产生
=
nT0
nG 个帧均匀的产生在nT0时间内,n
==
=
最大

## Slide 29: CSMA (carrier sense multiple access)
simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless (CSMA/CA) collision avoidance
human analogy: the polite conversationalist

## Slide 30: CSMA: collisions
collisions can still occur with carrier sensing:
  propagation delay means two nodes may not hear each other’s just-started transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 31: CSMA/CD:
CSMA/CD reduces the amount of time wasted in collisions
  transmission aborted on collision detection
  The packet transmission must be sufficiently long to detect collision (why?)
  2 signal propagation time
spatial layout of nodes
Abnormal detected signal energy when collision occurs

## Slide 32: CSMA/CD:
Collision
Collision detected
Jamming signal:
a random bit sequence that makes the receiver drops the packet (failed CRC check)
Jamming signal
Data frame
Data frame

## Slide 33: Ethernet CSMA/CD algorithm
NIC receives datagram from network layer, creates frame
If NIC senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If NIC transmits entire frame without collision, NIC is done with frame !
If NIC detects another transmission while sending: abort, send jam signal
After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval
  Drop the packet after M collisions

## Slide 34: 以太网CSMA/CD算法
适配器获取数据报，创建帧
发送前：侦听信道CS
  闲：开始传送帧
  忙：一直等到闲再发送
发送过程中，冲突检测CD，如果没有冲突: 成功
如果检测到冲突: 放弃，发送干扰信号，之后尝试重发
  所有听到冲突的适配器也发干扰信号，强化冲突：让所有站点都知道冲突
如果放弃，适配器进入指数退避状态(binary exponential backoff)
  在第m次失败后，适配器在退避区间个 {0,1,2, …, 2m-1}随机选择一个K. 等待发送 K·512 bit的时间, 转到步骤2。
  更多的冲突：更长的退避区间
  在M次冲突后，放弃该数据包

## Slide 35: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 36: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!
  No collision and idle slot

## Slide 37: “Taking turns” MAC protocols
polling:
master node “invites” other nodes to transmit in turn
typically used with “dumb” devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 38: “Taking turns” MAC protocols
token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 39: Cable access network: FDM, TDM and random access!
cable headend
CMTS
ISP
cable modem
termination system
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
multiple downstream (broadcast) FDM channels: up to 1.6 Gbps/channel
  single CMTS transmits into channels
multiple upstream channels (up to 1 Gbps/channel)
  multiple access: all users contend (random access) for certain upstream channel time slots; others assigned TDM

## Slide 40: Cable access network:
DOCSIS: data over cable service interface specification
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
Residences with cable modems
Downstream channel i
Upstream channel j
MAP frame for
Interval [t1, t2]
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS

## Slide 41: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 42: Review Questions:
Suppose two nodes start to transmit at the same time a packet of length L over a broadcast channel of rate R. Denote the propagation delay between the two nodes as d_prop. Will there be a collision if d_prop<L/R? Why or why not?

## Slide 43: Review Questions:
Suppose two nodes start to transmit at the same time a packet of length L over a broadcast channel of rate R. Denote the propagation delay between the two nodes as d_prop. Will there be a collision if d_prop<L/R? Why or why not?
There will be a collision in the sense that while a node is transmitting it will start to receive a packet from the other node.

## Slide 44: Review Questions:
In CSMA/CD, after the fifth collision, what is the probability that a node chooses K=4? The result corresponds to a delay of how many seconds on a 10 Mbps Ethernet?

## Slide 45: Review Questions:
In CSMA/CD, after the fifth collision, what is the probability that a node chooses K=4? The result corresponds to a delay of how many seconds on a 10 Mbps Ethernet?
After the 5th collision, the adapter chooses from {0, 1, 2,…, 31}. The probability that it chooses 4 is 1/32. It waits 204.8 microseconds.

## Slide 46: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 47: MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD

## Slide 48: MAC addresses
each interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address (as we’ve seen)
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or wireless)
137.196.7/24
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23

## Slide 49: MAC addresses
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like National Identity Number
  IP address: like postal address
MAC flat address: portability
  can move interface from one LAN to another
  recall IP address not portable: depends on IP subnet to which node is attached
  IP地址是有层次的：不能移动

## Slide 50: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)

## Slide 51: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)

## Slide 52: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)

## Slide 53: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500

## Slide 54: Routing to another subnet: addressing
walkthrough: sending a datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame) levels
R
A
B
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
  assume that:
    A knows B’s IP address
    A knows IP address of first hop router, R (how?)
    A knows R’s MAC address (how?)

## Slide 55: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame containing A-to-B IP datagram
  R's MAC address is frame’s destination
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 56: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 57: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
IP
Eth
Phy

## Slide 58: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
transmits link-layer frame
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address

## Slide 59: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
B receives frame, extracts IP datagram destination B
B passes datagram up protocol stack to IP
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 60: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 61: Ethernet
“dominant” wired LAN technology:
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 400 Gbps
single chip, multiple speeds (e.g., Broadcom BCM5761)
Metcalfe’s Ethernet sketch
https://www.uspto.gov/learning-and-resources/journeys-innovation/audio-stories/defying-doubters

## Slide 62: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
switched: prevails today
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)

## Slide 63: Ethernet frame structure
sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
preamble:
used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011

## Slide 64: Ethernet frame structure (more)
dest.
address
source
address
data (payload)
CRC
preamble
type
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk; ARP also has a type number
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped

## Slide 65: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn’t send ACKs or NAKs to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 66: 802.3 Ethernet standards: link & physical layers
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps

## Slide 67: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 68: Ethernet switch
Switch is a link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links
  when frame is to be forwarded on segment(网段), uses CSMA/CD to access segment
  通常一个交换机端口连接一个独立网段
transparent: hosts unaware of presence of switches
  通过交换机相联的各节点好像这些站点是直接相联的一样
  host/router addresses a frame to another host/router (rather than addressing the frame to the switch)
  unaware that a switch will be receiving the frame and forwarding it.
plug-and-play, self-learning
  switches do not need to be configured

## Slide 69: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  但A-to-A’和 C-to-A’不能同时传输

## Slide 70: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  but A-to-A’ and C to A’ can not happen simultaneously

## Slide 71: Switch forwarding table
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
  A: 交换机自学习(self-learning)

## Slide 72: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 73: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 74: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
frame destination, A’, location unknown:
flood
destination A location known:
selectively send
on just one link

## Slide 75: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 76: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 77: Small institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 78: Switches vs. routers
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6-78
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses

## Slide 79: 交换机 vs 路由器
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6-79
都是存储转发设备，但层次不同
交换机：链路层设备（检查链路层头部）
路由器：网络层设备（检查网络层的头部）
都有转发表：
交换机:
  通过洪泛、自学习来生成MAC地址转发表
  即插即用
  局部转发表
路由器:
  通过路由算法生成IP地址转发表
  限制分组广播
  不是即插即用，需要配置网络地址
  全局转发表

## Slide 80
如果主机F发送数据帧到A，哪些交换机收到了该信息？主机E能收到吗？
在主机F发送之后，如果主机B发送数据帧到主机F，哪些交换机收到了该信息？主机E能收到吗？
假设紧接着b),主机D向主机B发送数据帧，哪些交换机收到了该信息？主机E能收到吗？

## Slide 81
如果主机F发送数据帧到A，哪些交换机收到了该信息？主机E能收到吗？
交换机3 2 1 4
E可以收到
在主机F发送之后，如果主机B发送数据帧到主机F，哪些交换机收到了该信息？主机E能收到吗？
交换机 1 2 3 4
E收不到
假设紧接着b),主机D向主机B发送数据帧，哪些交换机收到了该信息？主机E能收到吗？
交换机 1 2 3
E收不到

## Slide 82: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 83: Virtual LANs (VLANs): motivation
Computer
Science
EE
Q: what happens as LAN sizes scale, users change point of attachment?
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy issues

## Slide 84: Virtual LANs (VLANs): motivation
administrative issues:
CS user moves office to EE - physically attached to EE switch, but wants to remain logically attached to CS switch
Computer
Science
EE
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy issues
Q: what happens as LAN sizes scale, users change point of attachment?

## Slide 85: Port-based VLANs
1
8
2
7
9
16
10
15
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local Area Network (VLAN)
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
… operates as multiple virtual switches
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)

## Slide 86: Port-based VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 87: VLANS spanning multiple switches
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removes additional header fields for frames forwarded between trunk ports

## Slide 88: 802.1Q VLAN frame format
802.1 Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information
(12 bit VLAN ID field, 3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 89: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 90: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router

## Slide 91: 802.11: Channels, association
spectrum divided into channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
arriving host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  then may perform authentication
  then typically run DHCP to get IP address in AP’s subnet
BSS

## Slide 92: IEEE 802.11 Wireless LAN
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and have base-station and ad-hoc network versions

## Slide 93: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with detected ongoing transmission by another node
802.11: no collision detection!
  difficult to sense collisions: high transmitting signal, weak received signal due to fading
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/CollisionAvoidance
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 94: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle; if busy, freeze the timer and continue count down when idle
3 transmit when timer expires
  If ACK received, successful transmission, transmit the next packet
  if no ACK, increase random backoff interval (binary exponential backoff as CSMA/CD), repeat 2
  Comparisons with CSMA/CD when two nodes sensed the channel idle?
  Transmit immediately vs count down

## Slide 95: Avoiding collisions (more)
May still collide with two nodes counting down to zero at the same time and hidden terminal problem
solution: sender “reserves” channel use for data frames using small reservation packets
sender first transmits small request-to-send (RTS) packet to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions (solves hidden terminal problem)
RTS
CTS
H1 is hidden from H2
H1 defers transmission on hearing CTS

## Slide 96: Collision Avoidance: RTS-CTS exchange
AP
A
B
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer
time

## Slide 97: Personal area networks: Bluetooth
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
2.4-2.5 GHz ISM radio band, up to 3 Mbps
master controller / clients devices:
  master polls clients, grants requests for client transmissions
radius of
coverage
C
C
C
P
P
P
P
M
C
master device
client device
parked device (inactive)
P
M

## Slide 98: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
  WiFi: 802.11 wireless LANs
link virtualization: MPLS

## Slide 99: Multiprotocol label switching (MPLS)
label
Exp
S
TTL
20
3
1
5
goal: high-speed IP forwarding among network of MPLS-capable routers, using fixed length label (instead of shortest prefix matching)
  faster lookup using fixed length identifier
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
remainder of Ethernet frame, including IP header with IP source, destination addresses
MPLS header
Ethernet
header
remainder of Ethernet frame, including IP header with IP source, destination addresses

## Slide 100: MPLS capable routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths

## Slide 101: MPLS versus IP paths
R2
D
R3
R5
A
R6
R4
IP routing: path to destination determined by destination address alone
IP router

## Slide 102: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
R4
IP routing: path to destination determined by destination address alone
IP/MPLS router
IP/MPLS entry router (R4) can use different MPLS routes to A based, e.g., on IP source address or other fields
MPLS routing: path to destination can be based on source and destination address
  flavor of generalized forwarding (MPLS 10 years earlier)
  fast reroute: precompute backup routes in case of link failure
R1

## Slide 103: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing:
  e.g., link bandwidth, amount of “reserved” link bandwidth
R2
D
R3
R5
A
R6
R4
modified
link state
flooding
RSVP-TE
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
R1

## Slide 104: MPLS forwarding tables
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
8 6 A 0
in out out
label label dest interface
10 A 0
12 D 0
8 A 1
R2
D
R3
R5
A
R6
R4
R1
0
1
0
0
1
0
Conventional IP based Routers
MPLS-enabled routers
By assigning different output label at R4 (10 or 8), packets can follow two different paths to destination A

## Slide 105: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS

## Slide 106: Synthesis: a day in the life of a web request
our journey down the protocol stack is now complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 107: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
arriving mobile client attaches to network …
requests web page: www.google.com
scenario:
Sounds
simple!

## Slide 108: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 109: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 110: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply

## Slide 111: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS

## Slide 112: A day in the life…TCP connection carrying HTTP
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)

## Slide 113: A day in the life… HTTP request/reply
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 114: Chapter 6: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation, implementation of various link layer technologies
  Ethernet
  switched LANS, VLANs
  virtualized networks as a link layer: MPLS
synthesis: a day in the life of a web request